## Slide 1: ECE 720T5 Fall 2012 Cyber-Physical Systems
Rodolfo Pellizzoni

## Slide 2: Today’s Outline
Cyber-Physical Systems: different views
Intro to Real-Time Systems
  Some knowledge of Real-Time is needed to read the papers.
  Get people with no experience in Real-Time Systems up to speed!
  One lecture only, so no time to go into details – please stop me if you don’t get it!

## Slide 3: Administrative Matters
If you are taking the course for credit: by this Friday, please email me and let me know which track you wish to follow.
Applied track: schedule a meeting next week to get you started on the project (suggested: Thursday 27).
Research track: if you are looking for research ideas on the project, please contact me asap. Otherwise, we will schedule a meeting on the week of October 1 (proposal due Oct 8 early morning).

## Slide 4: Cyber-Physical Systems: Different Views
Edward Lee. CPS: Design Challenges
  Abstraction problem
  Concurrent programming languages and timing models?
  Redesign embedded architectures?

## Slide 5: Intro to Real-Time Systems
Rodolfo Pellizzoni

## Slide 6: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 7: Books
J. Liu: Real-Time Systems. Prentice Hall, 2000.
  Best as an intro book, less good as a reference.
G.C. Buttazzo: Hard Real-Time Computing Systems: Predictable Scheduling Algorithms and applications. Springer, 2004.
  Good reference on real-time scheduling.
No good book reference for multiprocessor systems.

## Slide 8: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 9: Real-Time Systems
The correctness of the system depends not only on the logical result of the computation but also on the time at which the results are produced.
A correct value at the wrong time is a fault.
Processes attempt to control or react to events that take place in the outside world
These events occur in “real time” and tasks must be able to keep up with them
Processes are associated with timing constraints (deadlines)

## Slide 10: Soft vs Hard Real-Time
Soft real-time: missing deadlines is undesirable, but will not lead to catastrophic consequences
  Related to the concept of “Quality of Service”
  Typically interested in average-case response time (turnaround time)
  Ex: reservation systems, media players, phones, etc.
Hard real-time: missing deadlines is not an option
  Interested in worst-case response time
  Ex: airplanes, nuclear plants, military systems, etc.
  However, more on control performance later…

## Slide 11: Real-Time Spectrum
User interface
Computer simulation
Internet video, audio
Tele communication
Flight control
Soft RT
Hard RT
No RT

## Slide 12: Task Model
Task: a real-time computation unit
  Think of it as an execution thread with additional timing parameters (in particular: service time is known).
  The job of the real-time scheduler is to schedule tasks.
Three main task models:
  Aperiodic
  Periodic
  Sporadic

## Slide 13: Aperiodic Tasks
Event-triggered computation.
Task is activated by an external event.
Task runs once to respond to the event.
Relative deadline D: available time to respond to the event.
Ex: event = loss of power. Task = drop control rods into nuclear reactor (this actually happened at Fukushima)

## Slide 14: Periodic Task
Time-triggered computation
Task is activated periodically every T time units.
Each periodic instance of the task is called a job.
Each job has the same relative deadline (usually = to period).
Ex: most digital controllers.
Sporadic task: same as periodic task, but the task is activated at most every T time units (minimum interarrival time).
Ex: processing network packets.

## Slide 15: Periodic Task – Main Concepts
Task τi (N tasks in the system, τ1 to τN)
  Execution time Ci (sometimes ei)
  Relative deadline Di
  Period Ti (sometimes pi)
Each job τij of τi (first job: τi0)
  Activation time aij = aij-1 + Ti (usually with ai0 = 0)
  Sporadic: aij >= aij-1 + Ti
  Absolute deadline dij = aij + Di

## Slide 16: Periodic Task – Main Concepts
Task τi (N tasks in the system, τ1 to τN)
  Execution time Ci (sometimes ei)
A good portion of the course: How do we compute this?

## Slide 17: Periodic Task Model
ai0=0
ai1=10
ai2=20
t
0
10
20
di0=8
di1=18
Ci=3
Di=8
Ti=10
response time for job#1: 6
τi
τi0
τi1

## Slide 18: Utilization & Schedulability Analysis
Task Utilization for a periodic/sporadic task: Ui = Ci / Ti.
  Percentage of processor time required by the task.
System Utilization: U = U1 + U2 + … + UN.
  Percentage of processor time required by all tasks.
Base uniprocessor scheduling result: task set is clearly not schedulable if: U > 1.
For many scheduling algorithms, we can define a utilization bound Ub such that the task set if schedulable if: U <= Ub.

## Slide 19: Other Details on the Analysis…
For a scheduling algorithm to be useful, it must be associated with a schedulability analysis.
Sufficient analysis: if analysis says YES, then task set is schedulable by the given algorithm. If the analysis says NO, we do not know.
Necessary analysis: if analysis says NO, then we know that there exists a valid scenario in which the task set misses a deadline.
Offline analysis: task set is decided before the system starts. Run schedulability analysis offline.
Admission control: new tasks can arrive at run-time. Run schedulability analysis on-line and admit new task only if all tasks can still meet deadlines

## Slide 20: Other Details on the Task Set…
Jitter Ji: job τij will be activated in the time window [aij , aij + Ji].
Can model unpredictability in the activation time or precedence constraints.
Synchronous task set: all jobs τi0 are activated simultaneously at ai0 = 0.
  In many cases this corresponds to the worst-case response time (critical instant).
  ai0 is the offset of τi0.
Asynchronous task set: if ai0 != 0 for some task.
If we do not specify: Offset free - we do not know the ai0 (in which case, assume the worst case).

## Slide 21: The Simplest Model
We first look at the simplest possible model, where:
  All tasks are periodic
  Single processor
  Tasks do not share any resource
Not very realistic, but instructive (we have simple results)!
We will then (briefly) look at:
  What happens when you start sharing resources
  What happens if you schedule a mix of periodic/aperiodic tasks.
  What happens if you use a multiprocessor
  More complex task models

## Slide 22: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 23: Uniprocessor Periodic Scheduling
Three main scheduling categories
Table-based scheduling
  Build a table that dictates when each task executes
  Problem: only works for periodic tasks
  Problem: only works for off-line analysis
  Sometimes the best choice for more complex task models
Fixed-priority scheduling
  Each task is assigned a fixed priority
Dynamic-priority scheduling
  Task priority varies at run-time (ex: each job of the task has a different priority)
Scheduler is typically preemptive – better system utilization

## Slide 24: Rate-Monotonic Scheduling
Fixed-priority scheduling algorithm
Assumes periodic or sporadic tasks with Di = Ti on a uniprocessor.
Assigns priorities to tasks on the basis of their periods: shorter period = higher priority.
Liu & Layland schedulability analysis: task set is schedulable if: U <= Ub(N) = N(21/N – 1)
Note that limN->+inf N(21/N-1) = log 2 ~= 0.693
What happens if Ub(N) < U <= 1?
  Nothing can be said according to the analysis
  Task set might or might not be schedulable

## Slide 25: RM Example
Worst-case response time is produced when ai0 = 0.
Case#1:
  τ1 (C1 = 4, T1 = 8), high prio, τ2 (C2 = 3, T1 = 12), low prio
  Utilization: U = 4/8 + 3/12 = 0.75 < Ub(2) ~=0.828
  Schedulability analysis: schedulable
t
0
10
20
τ2
t
τ1

## Slide 26: RM Example
Case#2:
  τ1 (C1 = 4, T1 = 8), high prio, τ2 (C2 = 4, T1 = 12), low prio
  Utilization: U = 4/8 + 4/12 ~= 0.833 > Ub(2) ~=0.828
  Schedulability analysis: we do not know
  In reality: it is schedulable
t
0
10
20
τ2
t
τ1

## Slide 27: RM Example
Case#3:
  τ1 (C1 = 4, T1 = 8), high prio, τ2 (C2 = 6, T1 = 12), low prio
  Utilization: U = 4/8 + 6/12 = 1 > Ub(2) ~=0.828
  Schedulability analysis: we do not know
  In reality: it is not schedulable
t
0
10
20
τ2
t
τ1
deadline miss

## Slide 28: Earliest-Deadline First
Dynamic-Priority Scheduling Algorithm
Task priority is inversely proportional to its current absolute deadline
  Earlier deadline = higher priority
  Each job of a task has a different deadline, hence a different priority.
Assumes synchronous or offset-free periodic or sporadic tasks with Di = Ti on a uniprocessor, then…
Schedulability analysis: the task set is schedulable if: U <= Ub = 1
  Since task sets with U > 1 can not be scheduled by any algorithm, EDF is optimal

## Slide 29: EDF Example
Case#3:
  τ1 (C1 = 4, T1 = 8), τ2 (C2 = 6, T1 = 12)
  Utilization: U = 4/8 + 6/12 = Ub = 1
  Schedulability analysis: schedulable
t
0
10
20
τ2
t
τ1

## Slide 30: Another Example
τ1 (C1 = 1, T1 = 4), τ2 (C2 = 2, T1 = 6), τ3 (C3 = 3, T3 = 8)
Utilization: U = 1/4 + 2/6 + 3/8 = 23/24
RM: don’t know (utilization bound), in reality: not schedulable

## Slide 31: Another Example
τ1 (C1 = 1, T1 = 4), τ2 (C2 = 2, T1 = 6), τ3 (C3 = 3, T3 = 8)
Utilization: U = 1/4 + 2/6 + 3/8 = 23/24
EDF: schedulable

## Slide 32: EDF vs RM
In practice, industrial systems heavily favor RM over EDF. Why?
For most task sets, RM has better utilization bound than log 2.
  There are more complex, necessary analysis.
  If task periods are harmonic (every period is an integer divisor of any larger period), then Ub = 1. This happens often in practice.
RM is easier to implement in systems with limited number of priority levels.
RM is more transparent – easier to understand what is going on if something goes wrong (ex: overload).
  I.e. if a task executes for longer than its prescribed worst-case time, higher priority tasks will be left untouched.

## Slide 33: Different deadlines assignments
What happens if Di != Ti ?
EDF still optimal.
Instead of RM, use DM – deadline monotonic (best among fixed priority algorithms).
If Di < Ti , utilization bound still works by changing periods to deadlines in the formula – however this is pessimistic.
There exist exact schedulability analyses for both EDF and fixed priority that can be applied whatever the deadline – but they are pseudo-polynomial.
There are also analyses for asynchronous task sets – but exact analysis is exponential.

## Slide 34: Fixed Priority – Exact Analysis
Iterative solution. Tasks ordered by decreasing priority.
Ri(k) : worst-case response time for τi at step k.
If the iteration converges -> fixed point represents the worst-case response time for the task.
Key idea: is the max # of jobs of τj that interferes with τi

## Slide 35: Fixed Priority – Exact Analysis
τ1 (C1 = 2, T1 = 5), τ2 (C2 = 2, T1 = 9), τ3 (C2 = 5, T1 = 20); U = 0.872 > Ub(3) = 0.780

## Slide 36: Fixed Priority – Exact Analysis
τ1 (C1 = 2, T1 = 5), τ2 (C2 = 2, T1 = 9), τ3 (C2 = 5, T1 = 20); U = 0.872 > Ub(3) = 0.780

## Slide 37: Fixed Priority – Exact Analysis
τ1 (C1 = 2, T1 = 5), τ2 (C2 = 2, T1 = 9), τ3 (C2 = 5, T1 = 20); U = 0.872 > Ub(3) = 0.780

## Slide 38: Fixed Priority – Exact Analysis
τ1 (C1 = 2, T1 = 5), τ2 (C2 = 2, T1 = 9), τ3 (C2 = 5, T1 = 20); U = 0.872 > Ub(3) = 0.780

## Slide 39: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 40: Mutual Exclusion and Priority Inversion
Real-time tasks often communicate through shared memory.
  Each shared data structure is called a resource.
Mutual exclusion is enforced by semaphores protecting critical sections A, B, … (sometimes S1, …, SK).
Priority inversion: high prio task is blocked (waits for) low prio task.
Priority inversion is inevitable…
… but if we use normal semaphores, we get unbounded priority inversion.

## Slide 41: Unbounded Priority Inversion
High prio task is delayed by execution of tasks outside critical sections.
w(A): lock semaphore (wait). s(A): unlock semaphore (signal).
t
0
10
20
τ3
t
τ2
t
τ1
: resource A
w(A)
s(A)
s(A)
w(A)
τ2 blocks τ1!

## Slide 42: Unbounded Priority Inversion
Is this a problem?
Yes! Mars Pathfinder crashed because of it.
Luckily, they “patched” the OS remotely.
t
0
10
20
τ3
t
τ2
t
τ1
: resource A
w(A)
s(A)
s(A)
w(A)
τ2 blocks τ1!

## Slide 43: Basic Priority Inheritance Protocol
Works for fixed-priority scheduling (ex: RM).
While τi blocks higher priority task τj, τi inherits the priority of τj.
Inheritance is transitive
  If τk blocks τi, τk inherits the priority of τj through τi.
Avoids both unbounded priority inversion and deadlock (the latter only if there are no nested resources).

## Slide 44: Example Priority Inheritance Protocol
t
0
10
20
τ3
t
τ2
t
τ1
: resource A
w(A)
s(A)
s(A)
w(A)
τ3 inherits
τ1 priority

## Slide 45: Example Priority Inheritance Protocol
t
0
10
20
τ3
t
τ2
t
τ1
: resource A
w(A)
s(A)
s(A)
w(A)
τ2 suffers indirect blocking here – blocked by τ3 because of a resource shared with τ1

## Slide 46: Nested Resources
t
0
20
τ4
t
τ2
t
τ3
: resource A
w(A)
τ1
: resource B
w(B)
s(B)
s(A)
τ1 prio
τ1 prio
τ3 prio
τ4 prio
w(A)
s(A)
s(B)
w(B)
Note τ4 gets
τ1 priority through transitive inheritance!

## Slide 47: Double Blocking
t
0
20
τ3
t
τ1
t
τ2
: resource A
w(A)
: resource B
s(A)
w(B)
s(A)
s(B)
w(B)
w(A)
s(B)
τ1 blocked by τ2
τ1 blocked by τ3

## Slide 48: PIP - Analysis
A task can be blocked at most once on each resource
A task can be blocked for at most the duration of a single critical section by each lower priority task.
Iterative procedure can be used to compute the blocking time Bi for each task based on the rules…
For FP with Di = Ti , sufficient schedulability analysis:

## Slide 49: Improving PIP
Problem: under PIP a task can be blocked multiple times.
Solution: restrict the ability of a middle-priority task from entering critical section.
Ex: Stack Resource Policy (also known as Immediate Priority Ceiling Protocol)
  Each resource is assigned a ceiling equal to the highest priority of any task using the resource
  A task can preempt lower priority tasks only if its priority is higher than the ceiling of all locked resources.
  Essential property: a task can be blocked by at most one critical section.
  Also works for EDF (with ceiling = 1/Di)

## Slide 50: Double Blocking
t
0
20
τ3
t
τ1
t
τ2
: resource A
w(A)
: resource B
s(A)
w(B)
s(A)
s(B)
w(B)
w(A)
s(B)
τ2 blocked by τ3
τ1 blocked by τ2
Ceiling of both resource = priority of τ1

## Slide 51: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 52: Aperiodic Tasks
What happens if we mix aperiodic and periodic tasks?
Main idea: ensure that periodic tasks remain schedulable no matter what.
Aperiodic server
  Insert aperiodic tasks into a queue (server)
  Scheduler picks among periodic tasks or the aperiodic server
Schedulerr
τN
τ1
τi
Aperiodics
Server
Processor
…
…

## Slide 53: Aperiodic Servers
Server Goals:
  Minimize response time of aperiodic tasks
  Low overhead
Solution#1: background server
Execute aperiodics whenever the CPU is not running a periodic task (i.e., the server has lowest priority)
Problem: response time can be very high.

## Slide 54: Aperiodic Servers
Solution#2: budget-based server
Server is assigned budget Qi and period Ti.
The server behaves like a periodic task with Ci = Qi and period Ti.
When the scheduler picks the server, if there is budget left, the server executes an aperiodic in the queue consuming its budget.
When budget = 0, server waits until the next period, then replenish the budget to Qi.
Problem: what happens if the scheduler picks the server and there are no queued aperiodic tasks?
  “Dumb” servers (polling server) lose budget.
  “Smart” servers (ex: sporadic server) keep the budget but modify their activation (recharge) time.

## Slide 55: Polling Server
55
t
t
τ1
t
τ3
t
budget
t
aperiodics
server
T2 = 8
Q2 = 2
1
2
drop all budget
immediately
0.5
wait replenishment

## Slide 56: Sporadic Server
56
t
t
τ1
t
τ3
t
budget
t
aperiodics
server
T2 = 8
Q2 = 2
1
2
consume budget when
no higher priority task
is running
0.5
Notes: There are additional rules not covered here…
You can think of the server as executing tau_3 in [9,9.5] – it’s essentially donating budget to a lower priority task

## Slide 57: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 58: Scheduling on Multiprocessor
Two solutions for scheduling real-time tasks on multiprocessors.
Solution #1: partitioning
  Statically assign tasks among M processors.
  Ex: EDF. Each core is schedulable if sum of utilizations of tasks assigned to that core <= 1.
  Problem can be rephrased as: given a set of objects with known sizes (task utilizations), place them into M equal-size containers.
  Classic bin-packing problem – NP-hard.

## Slide 59: Scheduling on Multiprocessor
Solution #2: global scheduling
  Keep a global scheduling queue.
  Whenever there is a free core, pick one task from the queue and schedule it on the core.
In practice, real-time adoption of multiprocessor is limited, especially for hard systems.
Partitioned scheduling preferred – three issues with global scheduling
  Increases unpredictability – tasks can migrate among cores
  Much more complex to implement
  Does not necessarily perform better than partitioned

## Slide 60: Global Scheduling
Problem: both fixed-priority and EDF scheduling perform poorly when there are long tasks.
t
0
10
τ3
t
τ2
t
τ1
: Processor A
: Processor B
τ3 is barely schedulable (EDF)
We are wasting one processors here

## Slide 61: Global Scheduling
Optimal algorithm: p-fair.
Split the tasks into small chunks.
Allocate them on the cores in a “fair” way.
t
0
9
τ3 (6,9)
t
τ2 (6,9)
t
τ1 (6,9)
: Processor A
: Processor B

## Slide 62: Global Scheduling
Pros: task set schedulable on M cores iff U <= M ; the algorithm is optimal.
Cons: this does not take into account the cost of preemption and migration.
t
0
10
τ3 (6,9)
t
τ2 (6,9)
t
τ1 (6,9)
: Processor A
: Processor B

## Slide 63: Scheduling on Multiprocessor
Some other details…
There are several (only sufficient) schedulability analyses for EDF and FP – both based on utilization bounds and response time…
There are extensions for resource sharing protocols and aperiodic servers to multicores…
Very active research topic, but often ignores the main problem – how do we determine the worst-case computation time?

## Slide 64: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 65: End-To-End Delay
So far we have considered periodically-activated tasks.
However, oftentimes tasks depend on communication messages.
Start on this cores…
…then send a message to a task on to this one…
..and finally another message to this core.
τ1
τ2
τ3

## Slide 66: End-To-End Delay
Key goal: compute End-To-End Delay.
Possible solution: use activation jitter.
Jitter J2 of τ2 : worst-case response time of τ1
Jitter J3 of τ3 : worst-case response time of τ2
t
0
10
20
τ3
t
τ2
t
τ1
J2
J3
message
message
End-to-end deadline

## Slide 67: End-To-End Delay
Can be solved with a brute-force iteration
  Start from jitters = 0
  Compute response times
  Update jitters, repeat until convergence
t
0
10
20
τ3
t
τ2
t
τ1
J2
J3
message
message
End-to-end deadline

## Slide 68: End-To-End Delay
We will look at more intelligent methods when we talk about timing analysis…
t
0
10
20
τ3
t
τ2
t
τ1
J2
J3
message
message
End-to-end deadline

## Slide 69: Outline
Introduction and Task Model
Uniprocessor Real-Time Scheduling
Priority Inversion and Resource Sharing
Aperiodic Task Scheduling
Multiprocessor Scheduling
The End-to-End Delay Problem
Scheduling and Control Quality

## Slide 70: Scheduling and Control Quality
We mentioned that typical periodic task = digital controller.
In practice, the quality of the control depends on:
  Frequency of sensing/actuation (i.e. frequency of control)
  Delay in actuation wrt sensing.
Scheduling decisions should take control quality into account…