## Slide 1: ECE 720T5 Winter 2014 Cyber-Physical Systems
Rodolfo Pellizzoni

## Slide 2: Administrative
Next week: project presentations.
  12 minutes per project + 3 minutes for questions.
  If you cannot stay the whole lecture, please let me know by email.
  Time is limited, so ensure you focus on: 1. overview of the project 2. what you set out to accomplish 3. what are your (preliminary) results.
  Class presentations end today – plan is to have all comments out by Thursday.

## Slide 3: Topic Today: Models & Verification
Remember verification: ensuring that a subsystem (or step in the design) meets the objectives for that subsystem, i.e. it does what we want it to do.
How to verify a system/subsystem?
  (Exhaustive) testing
  Formal verification

## Slide 4: Formal Verification: Key Issues
Modeling
  Formal verification verifies a model of the system, not the system implementation!
  Models must represents both hardware as well as software component.
  System-level verification – need architecture description language.
  How can different models (ex: differential equations and automata) interact?
Complexity
  Most applicable techniques scale poorly – allows only for verification of limited-scale subsystems.

## Slide 5: Example: Timed Automata
Finite-state Machines extended with timers.
  Timers are continuous – effectively infinite-state.
Time is explicit – very useful to model real-time systems.

## Slide 6: UPPAAL
Automatic verification of Real-Time Communicating Systems by Constraint-Solving.
Verification tool for real-time systems.
Model-checking based on composition of timed automata.
  Parallel timed automata can exchange signals.
  Determines whether the system can reach a particular state or set of states.
Very powerful property – model-checking can be reduced to verifying a set of linear constraints on clocks.

## Slide 7: Ex: Train Controller
Controller
Train i
Safety property: no two trains in their cross state
at the same time

## Slide 8: An Alternative Solution: Run-Time Monitoring
Divide the system is a set of simple, verifiable safety-critical components and a set of complex, untrusted components.
A formal requirement specification is attached to each unverified component.
The specification acts as a certificate: if the component behaves according to the specification, the system remain safe.
At run-time, we monitor (check) the actual component behavior against its requirement specification expressed as a set of properties.
If a requirement violation is detected, we perform a recovery action to restore the system to a safe state.
Key idea: it is simpler to check the certificate that to verify the inner working of the unverified component.

## Slide 9: The Big Picture: Event-Based Monitoring
Event Generator
E1
-
E2
E3
E1
-
-
t
Monitor
Handler (Recovery)
Violation /
Validation
Event Specification
Formula
The system to be
monitored (HW/SW)
2. User specifies a set of events.
Ex: a specified variable is modified
3. Event Generator generates a
trace of observed events over time.
4. User specifies a formula
using defined events.
Ex: (E1 E2) *
5. Monitor checks if formula is
validated / violated based on
event trace.
6. A recovery handler is
called if a validation /
violation is detected.
System

## Slide 10: Monitoring Overhead
Two main issues:
  How do we generate the events? Answer – architecture specific.
  Where do we run the monitors?
Most available frameworks use software-based solutions.
  Event generation hooks are inserted by the compiler into the code.
  Monitors are run in SW either on the same processor or a separate processor.
Problem: the overhead is typically not predictable – how many events gets generated?

## Slide 11: Predictable Monitoring Solutions
Sampling-based monitoring
  Instead of running the monitor every time an event is generated, sample the system periodically.
  Analysis is required to ensure that the sampling happens often enough to capture the properties of interest.
Hardware-base monitoring
  Required for HW components with no corresponding SW code
  Run both the event generator and the monitors in HW
  Potentially zero timing overhead (if done right)

## Slide 12: Cyberphysical System Runtime Verification

## Slide 13: Simplex Model
Run-time verification for Control Systems.
Under normal conditions, run a complex controller.
If the complex controller fails, switch to a simpler, verified one.

## Slide 14: Model: Hybrid Automata
Similar to timed automata + continuous state
  Discrete states and transitions
  Timers, guards on transitions, invariants on states
  New: continuous-state variables (ex: position, velocity, …)
  New: dynamic in each state (differential equations)

## Slide 15: Model: Hybrid Automata
Similar to timed automata + continuous state
  Discrete states and transitions
  Timers, guards on transitions, invariants on states
  New: continuous-state variables (ex: position, velocity, …)
  New: dynamic in each state (differential equations)

## Slide 16: How does it work?
Discretize the continuous state space.
From each discretized state space, compute the set of all reachable states in Delta time.

## Slide 17: How does it work?
Discretize the continuous state space.
From each discretized state space, compute the set of all reachable states in Delta time.

## Slide 18: How does it work?
Discretize the continuous state space.
From each discretized state space, compute the set of all reachable states in Delta time.

## Slide 19: Model Checking the System
Result: we reduce the model to a discrete system (automata).
  The automata does not need to keep implicit track of time – time is encoded in the transition overapproximation.
We can then apply standard model checking to check that safety is guaranteed – the system can never reach an unsafe state.
There are some constraints on the modeled dynamics…
  Most importantly, no cyclic dependencies among variables in the dynamic of the system modeled by dx/dt = F(x).
  Follow-up paper solves the problem…

## Slide 20: Case Study
Autonomous off-road vehicle.
John Deere is largest manufacturer of agricultural machinery.
Over 30 parameters in the vehicle model.
Goal: avoid roll-over.
Automatic generation of Decision Module in VHDL.