## Slide 1: ECE 720T5 Winter 2014 Cyber-Physical Systems
Rodolfo Pellizzoni

## Slide 2: Topic Today: End-To-End Analysis
HW platform comprises multiple resources
  Processing Elements
  Communication Links
SW model consists of multiple independent flows or transactions
  Each flow traverses a fixed sequence of resources
  Task = flow execution on one resource
  We are interested in computing its end-to-end delay
R1
R2
R3
R4
f1

## Slide 3: Analyses: Model
Analysis | Task Model | Resource Model | Arbitration | Deadlines
Network Calculus / Real-Time Calculus | General arrival model | General service model | Any; works better for independent policies | No assumption
Holistic Analysis | Periodic / Sporadic Transactions | Fixed times per-task | Independent (TDMA), FP, EDF | Any deadline
Delay Analysis | Aperiodic (can be extended to periodic but it works worse) | Fixed times per-task | Independent, FP | Any; for periodic, works better for D <= period
Flow-based latency analysis | Periodic / Sporadic Transactions | Fixed per-transaction time; no cycle | FP | <= period (could be extended)

## Slide 4: Pipeline Delay
f1 and f2 share more than one contiguous resources.
Can the analysis take advantage of this information?
  If f2 “gets ahead” of f1 on R2, it is likely to cause less interference on R3.
R1
R2
R3
R4
f1
f2

## Slide 5: Transitive Delay
f2 and f3 both interfere with f1, but only one at a time.
Can the analysis take advantage of this information?
R1
R2
R3
R4
f1
f2
f3

## Slide 6: Analyses: Model
Analysis | Interference increases with # resources? | Pipeline Delay Considered? | Transitive Delay Considered?
Network Calculus / Real-Time Calculus | Superlinear (down to almost constant in some cases) | No | Yes
Holistic Analysis | Generally linear in # different resources | No (partial if flow revisits resource) | Yes
Delay Analysis | Almost constant | Yes | No (partial extension)
Flow-based latency analysis | Almost constant | Yes | No (Yes for Link-Level Analysis)

## Slide 7: Holistic Analysis

## Slide 8: Transaction Model (Tasks with Offsets)
Schedulability Analysis for Tasks with Static and Dynamic Offsets.
Tighter Response Times for Tasks with Offsets

## Slide 9: Holistic Analysis
Start with offsets = cumulative computation times.
Compute worst-case response times.
Update release jitter.
Go back to step 2 until convergence to fixed-point (or end-to-end response time > deadline).

## Slide 10: Can you model Wormhole Routing?
Sure you can!
For a flow with K flits, simply assume there are K transactions
  Assign artificially decreasing priorities to the K transactions to best model the precedence constraint among flits.
The problem is that response time analysis for transaction models do not take into account relations among different resources – can not take advantage of pipeline delay.

## Slide 11: Response Time Analysis
Let’s focus on a single resource – note a flow might visit a resource multiple times.
The worst-case is produced when a task for each interfering transaction is released at the critical instant after suffering worst-case jitter.
  Tasks activated before the critical instant are delayed (by jitter) until the critical instant if feasible
  Tasks activated after the critical instant suffer no jitter
EDF: the task under analysis has deadline = to the deadline of any interfering task in the busy period
RM: a task of the transaction under analysis is released at the critical instant
  Same assumptions for all other tasks of the transactions
  In both cases, we need to try out all possibilities

## Slide 12: Response Time Analysis
Problem: the number of possible activation patterns is exponential.
  For each interfering transaction, we can pick any task.
  Hence the number of combinations is exponential in the number of transactions.
Solution: compute a worst-case interference pattern over all possible starting tasks for a given interfering transaction.
For the transaction under analysis we still analyze all possible patterns.

## Slide 13: Example
Transaction under analysis:
single task with C = 2

## Slide 14: Tighter Analysis
Key idea: use slanted
stairs instead

## Slide 15: Removing Jitter
Jitters introduce variability – increase w-case response time
Alternative: time-trigger all tasks.
Start with offsets = cumulative computation times.
Compute worst-case response times.
Modify offsets.
Go back to step 2 until convergence or divergence
However convergence is trickier now!

## Slide 16: Cyclic-Dynamic Offsets
Response time can decrease as a result of modifying offsets.
  Always increasing as jitter increases
We can prove that it is sufficient to check for limit cycles.

## Slide 17: Pipeline Delay
T2 higher priority. All Ctime = 1. With Jitter…
O = 0
R = 2
J = 0
O = 2
R = 7!
J = 2
O = 1
R = 4
J = 1
O = 4
R = 11
J = 5
O = 5
R = 13
J = 6
O = 6
R = 15
J = 7
O = 3
R = 9
J = 4

## Slide 18: Pipeline Delay
T2 higher priority. All Ctime = 1. With Offsets…
O = 0
R = 2
O = 4
R = 6
O = 2
R = 4
O = 8
R = 10
O = 10
R = 12
O = 12
R = 14
O = 6
R = 8

## Slide 19: Delay Calculus

## Slide 20: Delay Calculus
End-To-End Delay Analysis of Distributed Systems with Cycles in the Task Graph
System Model:
  Aperiodic flows (each called a job)
  Each job has the same fixed priority on all resources (nodes)
  Arbitrary path through nodes (stages) – can include cycles
  Each stage can have a different computation time
How to model worm-hole routing
  Use one job for each flit

## Slide 21: Break the Cycles
f1 lowest-priority flow under analysis
f2 is broken into two non-cyclic folds: (1, 2, 3) and (2, 3, 4)
The two segments that overlaps with f1 are: (1, 2, 3) and (2, 3)
Solution: consider f1(1, 2, 3) and f1(2,3) as separate flows.
R1
R2
R3
R4
f2
f1

## Slide 22: Types of Interfering Flows

## Slide 23: Execution Trace
Earliest trace: earliest job finishing time on each stage such that there is no idle time at the end.

## Slide 24: Delay Bounds
Each cross-flow segment and reserve-flow segment contributes one stage computation time to the earliest trace
What about forward flows?
S1
f1
f2
S2
f1
f2
S3
f2
S4
f2
f1
f1
f2 on the last stage
it delays f1
f2 preempting lower-priority job
one execution of the longest
job on each stage

## Slide 25: Delay Bounds
Preemptive Case:
Non-Preemptive Case:
2 max executions for each
higher priority segment
Max exec time
for each stage
No preemption means
one max execution for
higher priority segment…
… but we have to pay one
max execution of blocking time
on each stage

## Slide 26: Pipeline Delay - Preemptive
T2 higher priority. All Ctime = 1. T1 response time = 9.

## Slide 27: The Periodic Case
Now assume jobs are produced by periodic activations…
Trick: reduce cyclic system to an equivalent uniprocessor system. For preemptive case:
  Replace each segment with a periodic task with ctime =
  Replace the flow under analysis with a task with ctime =
Schedulability can then be checked with any uniprocessor test (utilization bound, response time analysis).

## Slide 28: Transitive Delay
All Ctime = 1, non-preemptive.
Let’s assume T2 = T3 = 2, deadline = period.
Then U2 = ½, U3 = ½ and the system is not schedulable…
In reality the worst-case response time of f1 is 4.
S1
S2
f1
f2
f3

## Slide 29: Other issues…
What happens if deadline > period?
  Add an addition floor(deadline/period) instances of the higher priority job.
  Self blocking: the flow under analysis can block itself. Hence, consider its previous instances as another, higher priority flow.
What happens if a flow suffers jitter (i.e., indirect blocking)?
  Add an additional ceil(jitter/period) instances.
  Note: all reverse flows have this issue…
Lots of added terms -> bad analysis for low number of stages.

## Slide 30: When does it perform well?
Send request to a server, get answer back.
Same path for all request/response pairs!
Hundreds of tasks.

## Slide 31: Deterministic Queuing

## Slide 32: Network and Real-Time Calclus
A deterministic version of classic queuing theory.
  Produces worst-case/best case bounds on latency and buffer size.
  A formal analysis for distributed embedded systems.
Different versions…
  Network calculus: worst-case only.
  Real-time calculus: best/worst case curves.
Proofs tend to be easier in real-time calculus version (due to definition of service curves)…

## Slide 33: Modular Performance Analysis
System Architecture evaluation using modular performance analysis: a case study
An application of real-time calculus to early system performance analysis and design exploration.
A more structured approach to system description and multiple flows analysis
Next: see slides at http://www.tik.ee.ethz.ch/education/lectures/hswcd/slides/11_ModularPerformanceAnalysis.pdf for real-time calculus basics.

## Slide 34: Concatenation
Two concatenated GPC.
Since convolution is associative:
In other words, we can substitute the two GPC for one GPC with lower service curve .
The resulting delay is better!

## Slide 35: Concatenation Example
If we consider each GPC individually:

## Slide 36: Concatenation Example
Note: if , the infimum is obtained by taking .
If , by setting .
In either cases, the function is equal to 0 until .

## Slide 37: Concatenation Result
We obtained a combined delay:
From previous slide:
Result: with concatenation, we pay the burstiness ( ) only once.

## Slide 38: Concatenation: Algorithm
Let , be input/output service curves for n GPC traversed by the flow under analysis.
Let be the input arrival curve for the flow, the output arrival curve for the i-th GPC.
Set .
For each GPC from i to n:
  Compute Bi and based on and .
  (For i > 1) Compute .
  (For i < n) Compute based on and .
Finally, compute D based on and .

## Slide 39: Concatenation Algorithm: Example
Note: buffer size computation not shown for simplicity.
  GPC 1
  GPC 2
  GPC 3
  Delay computation

## Slide 40: Aggregate Traffic
Assumption: we do not know the arbitration employed by the router.
Solution: consider each flow as the lowest-priority one.

## Slide 41: Network Solution
Problem: the burstiness values at stages 1, 2 are interdependent.
Solution: write a system of equations

## Slide 42: Network Stability
We need to compute
I - A can be inverted iff all eigenvalues of A have module <= 1.
The eigenvalues of the matrix are and .
Solving for rho:
Note: for bus utilizations > 76.4%, we can not find a solution.
Does a solution exist in such a case?
  Yes, following delay calculus, each bit of f1 can only delay f2 on one node.
  However, for more complex topologies (transitive delay) this is an open problem.

## Slide 43: Modular Performance Analysis

## Slide 44: Another Example: Real-Time Bridge
Incoming flow
Outgoing flow,
Network A
Outgoing flows,
Network B
Sporadic
Server
(reservations)
Bus
Scheduling
Network Transmission
Scheduling

## Slide 45: Design Flow

## Slide 46: Case Study: Radio Navigation System

## Slide 47: Example: Change Volume Sequence Diagram

## Slide 48: Architectural Alternatives

## Slide 49: Model: Architecture A

## Slide 50: End-To-End Delay

## Slide 51: Sensitivity to Resource Capacity