## Slide 1: PRET DRAM Controller: Bank Privatization for Predictability and Temporal Isolation
By Edward A. Lee, J.Reineke, I.Liu, H.D.Patel, S.Kim
Presented by: Michael Guo

## Slide 2: Outline
DRAM background information
Design Requirement
DRAM controller architecture
  Frontend
  Backend
Design Evaluation
Experiment
Further Improvement

## Slide 3: DRAM Memory Architecture

## Slide 4: DRAM Memory Architecture
DRAM Cell
  Consists of a capacitor and a transistor
  Charge of Capacitor determines the value of the bit
  Leak charge over time
DRAM Array
  Phase1: Row access followed by column access
  Phase2: Row access move one rows of array into row buffer

## Slide 5: DRAM Memory Architecture
DRAM Device and DRAM module
  Sharing of I/O gating and control logic
  Sharing of data/address/command buses

## Slide 6: Challenges for embedded hard-real time system
The platform should be timing predictable to make the verification of timing constraints possible.
  DRAM: The DRAM cells have to be refreshed periodically
Different functions integrated on the platform should be temporally isolated.
  DRAM: The latency of one task has high dependency on the previous access to the memory.

## Slide 7: PTARM PRET architecture
Implemented the controller on the PTARM PRET architecture proposed in [4]
Figure4: Integration of PTARM core with DMA units, PRET memory controller and dual-ranked DIMM

## Slide 8: PTARM PRET architecture
Thread-interleaved implementation of ARM instruction set
Four pipeline stages and four hardware thread
Each thread has access to an shared instruction scratchpad and data scratchpad
Thread can interact with DRAM directly or transferring data to and from the scratchpad
Summary: no dependencies between pipeline stages, and the execution time of each thread is independent from each other

## Slide 9: DRAM Module
General structure
  One resource
Proposed structure
  Independent resources

## Slide 10: DRAM Controller Backend
Issues commands
Implementation

## Slide 11: Access Scheme

## Slide 12: DRAM Controller Frontend
Connects to the Processor
PURPOSE: route requests to the right request buffer in the backend and to insert a sufficient amount of refresh commands

## Slide 13: Scheduling of Refreshes
  64ms timing constrain for the DRAM to refresh all the cells to restore the value
  Issue a hardware refresh command
    refresh several rows of a device at once
    ISSUE: increasing refresh latency
  Individual row accesses
    Each refresh accesses one row
    Advantage: single row access takes less time than the execution of a hardware refresh command
    Disadvantage: more manual row accesses have to be performed, lead a hit in bandwidth

## Slide 14: Store Buffer
Does not have to wait until the store has been performed in the memory
Hide the store latency from the pipeline
Single thread cycle if no preceded store
Bigger store buffer could hid latencies of successive stores at the expense of increased complexity in timing analysis.

## Slide 15: Latency of Load Instruction
Backend latency: BEL
  Time a command spends in the command buffer before the RAS command has been sent out
  DRAM Read latency: DRL
  After RAS sent to the DRAM module, it takes time until the request data is on the data bus
  Constant, 10+BL/2 cycles (to isolate from other effect)
  Thread Alignment Latency: TAL
  Time that the data is buffered in the memory controller
  Requesting thread can only receive the data in its write-back stage
  Read latency: RL
  RL = BEL + DRL + TAL

## Slide 16: Latency of Load Instruction
By delaying refreshes until a load has been performed, they do not have an impact on the load latency.

## Slide 17: Compare with Predator
DRAM as one resource
Use standard refresh mechanism
Pre-computed sequences of SDRAM commands

## Slide 18: Latency of DMA Transfer (Small size)

## Slide 19: Latency of DMA Transfer (Large size)

## Slide 20: EXPERIMENTAL EVALUATION
PTARM simulator to interface with both controller to run synthetic benchmark to compare memory access latency
Show the effects of interference on memory access latency with a combination of two programs on the other hardware threads.

## Slide 21: Demonstrate the temporal isolation achieved by the PRET DRAM controller

## Slide 22: Full load

## Slide 23: Conclusion and Limitation
The controller reduced the worst-case latency at a slight loss of bandwidth
Proposed solution has the same amount of hardware thread as the pipeline stages. If there is many thread, there has to many memory partitions
The consumption of bandwidth is not well analyzed

## Slide 24: Integration with other multiprocessor
Challenge
  Most multi-core processors use DRAM to share data, while local scratchpad are private
Approach
  Consider the four separate resource as one. An access to the single resource would result in four smaller accesses to the resources

## Slide 25: QUESTION