## Slide 1: ECE 720T5 Fall 2011 Cyber-Physical Systems
Rodolfo Pellizzoni

## Slide 2: Topic Today: Heterogeneous Systems
Modern SoC devices are highly heterogeneous systems - use the best type of processing element for each job
Good for CPS – processing elements are often more predictable than GP CPU!
Challenge #1: schedule computation among all processing units.
Challenge #2: I/O & interconnects as shared resources.
NVIDIA Tegra 2 SoC

## Slide 3: Processing Elements
Trade-offs of programmability vs performance/power consumption/area.
Not always in this order…
Application-Specific Instruction Processors
Graphics Processing Unit
Reconfigurable Field-Programmable Gate Array
Coarse-Grained Reconfigurable Device
I/O Processors
HW Coprocessors

## Slide 4: Processing Elements
Application-Specific Instruction Processors
  The ISA and microarchitecture is tailored for a specific application.
  Ex: Digital Signal Processor.
  Sometimes “instructions” invoke HW coprocessors.
Graphics Processing Unit
  Delegate graphics computation to a separate processor
  First appear in the ’80, until the turn of the century GPUs were HW processors (fixed functions)
  Now GPUs are ASIP – execute shader programs.
  New trend: GPGPU – execute computation on GPU.

## Slide 5: Processing Elements
Reconfigurable FPGA
  Logic circuits that can be programmed after production
  Static reconfiguration: configure FPGA before booting
  Dynamic reconfiguration: change logic at run-time
  More on this later if we have time…
Coarse-Grained Devices
  Similar to FPGA, but the logic is more constrained.
  Device typically composed of word-wide reconfigurable blocks implementing ALU operations, together with registers, mux/demux and programmable interconnects.

## Slide 6: Processing Elements
HW Processors
  ASIC logic block executing a specific function.
  Directly connected to the global system interconnects.
  Typically an active device (i.e., DMA capable).
  Can be more or less programmable.
  Ex#1: cellular baseband decoders – not programmable
  Ex#2: video decoder – often highly programmable (sometimes more of an ASIP)
I/O Processor
  Same as before, but dedicated to I/O processing.
  Ex: accelerated Ethernet NICs – move some portion of the TPC/IP stack in HW.

## Slide 7: GPU for Computation
Next: computation on GPU.

## Slide 8: I/O and Peripherals
What about peripherals and I/O?
Standardized Off-Chip Interconnects are popular
  PCI Express
  USB
  SATA
  Etc.
Peripherals can interfere with each other on off-chip interconnects!
  Dangerous if assigned different criticalities
  We can not schedule peripherals like we do for tasks

## Slide 9: Real-Time Control of I/O COTS Peripherals for Embedded Systems
Stanley Bak, Emiliano Betti, Rodolfo Pellizzoni, Marco Caccamo, Lui Sha
University of Illinois at Urbana-Champaign

## Slide 10
Embedded systems are increasingly built by using Commercial Off-The-Shelf (COTS) components to reduce costs and time-to-market
This trend is true even for companies in the safety-critical avionic market such as Lockheed Martin Aeronautics, Boeing and Airbus
COTS components usually provide better performance:
  SAFEbus used in the Boing777 transfers data up to 60 Mbps, while a COTS interconnection such as PCI Express can reach higher transfer speeds (over three orders of magnitude)
COTS components are mainly optimized for the average case performance and not for the worst-case scenario.
COTS HW & RT Embedded Systems
2

## Slide 11
According to ARINC 653 avionic standard, different computational components should be put into isolated partitions (cyclic time slices of the CPU).
ARINC 653 does not provide any isolation from the effects of I/O bus traffic. A peripheral is free to interfere with cache fetches while any partition (not requiring that peripheral) is executing on the CPU.
To provide true temporal partitioning, enforceable specifications must address the complex dependencies among all interacting resources.
 See Aeronautical Radio Inc. ARINC 653 Specification. It defines the Avionics Application Standard Software Interface.
ARINC 653 and unpredictable I/O behaviors
3

## Slide 12: Example: Bus Contention (1/2)
Modern COTS system comprising multiple buses.
High-performance DMA peripherals autonomously transfer data to/from Main Memory.
Multiple possible bottlenecks.
CPU
North
Bridge
RAM
PCIe
South
Bridge
ATA
PCI-X
2/19

## Slide 13: Example: Bus Contention (1/2)
CPU
RAM
Modern COTS system comprising multiple buses.
High-performance DMA peripherals autonomously transfer data to/from Main Memory.
Multiple possible bottlenecks.
2/19

## Slide 14: Example: Bus Contention (2/2)
Transaction Length | Bandwidth (256B)
No interference | 596MB/s (100%)
128 bytes | 441MB/s (74%)
256 bytes | 346MB/s (58%)
512 bytes | 241MB/s (40%)
Two DMA peripherals transmitting at full speed on PCI-X bus.
Round-robin arbitration does not allow timing guarantees.
CPU
RAM
3/19

## Slide 15: Example: Bus Contention (2/2)
0
8
16
t
t
3
NO BUS SHARING
Two DMA peripherals transmitting at full speed on PCI-X bus.
Round-robin arbitration does not allow timing guarantees.
CPU
RAM
3/19
6

## Slide 16: Example: Bus Contention (2/2)
Two DMA peripherals transmitting at full speed on PCI-X bus.
Round-robin arbitration does not allow timing guarantees.
CPU
RAM
3/19
0
8
16
t
t
6
BUS CONTENTION, 50% / 50%
10
4

## Slide 17: Example: Bus Contention (2/2)
Two DMA peripherals transmitting at full speed on PCI-X bus.
Round-robin arbitration does not allow timing guarantees.
CPU
RAM
3/19
0
8
16
t
t
9
BUS CONTENTION, 33% / 66%
9

## Slide 18: The Need for an Engineering Solution
Analysis is possible but bounds are pessimistic and require the specification of many parameters.
Average case significantly lower than worst case.
  Main issue: COTS arbiters are not designed for predictability.
We propose engineering solutions to control peripheral traffic.
Main idea: we need to provide traffic isolation by scheduling peripherals on the bus, like we schedule tasks on CPU.
26

## Slide 19: The Main Idea: Implicit Schedule
Problem: COTS arbiters optimized for average case, not worst case.
Solution: do not rely on COTS arbiter, enforce implicit schedule: high-level agreement among peripherals.
CPU
RAM
5/19
0
8
16
t
t
9
BUS CONTENTION, 33% / 66%
9

## Slide 20: The Main Idea: Implicit Schedule
IMPLICIT SCHEDULE ENFORCEMENT
CPU
RAM
5/19
0
8
16
t
t
3
BLOCK
BLOCK
Problem: COTS arbiters optimized for average case, not worst case.
Solution: do not rely on COTS arbiter, enforce implicit schedule: high-level agreement among peripherals.
Notes: Say enforce macro schedule despite the fact low-level transactions just go throught with no contention.

## Slide 21: The Main Idea: Implicit Schedule
CPU
RAM
5/19
IMPLICIT SCHEDULE ENFORCEMENT
0
8
16
t
t
3
BLOCK
BLOCK
Problem: COTS arbiters optimized for average case, not worst case.
Solution: do not rely on COTS arbiter, enforce implicit schedule: high-level agreement among peripherals.
CHALLENGE: How can we enforce the implicit schedule with minimal hardware modifications?

## Slide 22: Real-Time I/O Management System
A Real-Time Bridge is interposed between each high-throughput peripheral and COTS bus.
The Real-Time Bridge buffers incoming/outgoing data and delivers it predictably.
Reservation Controller enforces global implicit schedule.
Assumption: all flows share main memory…
… only one peripheral transmit at a time.
CPU
North
Bridge
PCIe
South
Bridge
ATA
PCI-X
RT
Bridge
RT
Bridge
RT
Bridge
RT
Bridge
Reservation
Controller
RAM
6/19

## Slide 23: Reservation Controller
Reservation Controller receives data_rdyi information from Real-Time Bridges and outputs blocki signals.
Since only one peripheral is allowed to transmit at a time, I/O flow scheduling is equivalent to monoprocessor scheduling!
Question: can any monoprocessor scheduling algorithm be implemented?
Reservation Controller
data_rdy1
block1
data_rdy2
block2
. . .
data_rdyi
blocki
. . .
9/19
Notes: Before SW stack

## Slide 24: Scheduling Framework
We consider a general framework composed of a scheduler and multiple scheduling servers.
Each server computes scheduling parameters for a flow. The scheduler decides which server to execute.
We show that we can implement the class of active dynamic servers: server behavior depends only on task data_rdy information.
FP + Sporadic Server
EDF + Constant Bandwidth Server
EDF + Total Bandwidth Server
Server1
Scheduler (FP)
READY1
EXEC1
EXEC1 = READY1
EXEC2 = READY2 and
not EXEC1
EXECi = READYi and
not EXEC1 … and not EXECi-1
. . .
. . .
READY2
EXEC2
READYi
EXECi
. . .
. . .
10/19
data_rdy1
block1
data_rdy2
block2
data_rdyi
blocki
Server2
Serveri

## Slide 25: Real-Time Bridge
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
block
data_rdy
System + PCI
Host CPU
Main Memory
PCI
Controlled
Peripheral
FPGA
FPGA System-on-Chip design with CPU, external memory, and custom DMA Engine.
Connected to main system and peripheral through available PCI/PCIe bridge modules.
Memory
Controller
PCI Bridge
8/19

## Slide 26: Real-Time Bridge
The controlled peripheral reads/writes to/from Local RAM instead of Main Memory (completely transparent to the peripheral).
DMA Engine transfers data from/to Main Memory to/from Local RAM.
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
block
data_rdy
System + PCI
Host CPU
Main Memory
PCI
Controlled
Peripheral
FPGA
Memory
Controller
PCI Bridge
8/19

## Slide 27: Real-Time Bridge
DMA Engine connection to the Reservation Controller:
  data_rdy: active if the peripheral has buffered data to transmit.
  block: used by reservation controller to control data transfers.
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
block
data_rdy
System + PCI
Host CPU
Main Memory
PCI
Controlled
Peripheral
FPGA
Memory
Controller
PCI Bridge
8/19

## Slide 28: Example: Download
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
System + PCI
Host CPU
Main Memory
TEMAC
NIC
FPGA
Source
FIFO
Dest
FIFO
FPGA/Host Driver maintains packet buffer lists with addresses in Source/Destination FIFO.
Notes: Move after

## Slide 29: Example: Download
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
System + PCI
Host CPU
Main Memory
TEMAC
NIC
FPGA
Source
FIFO
Dest
FIFO
Incoming packets are written in source buffers.

## Slide 30: Example: Download
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
System + PCI
Host CPU
Main Memory
TEMAC
NIC
FPGA
Source
FIFO
Dest
FIFO
DMAEngine transfers packets while not blocked.

## Slide 31: Example: Download
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
System + PCI
Host CPU
Main Memory
TEMAC
NIC
FPGA
Source
FIFO
Dest
FIFO
Host Driver processes packets (ex: TCP/IP stack).

## Slide 32: Example: Download
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
System + PCI
Host CPU
Main Memory
TEMAC
NIC
FPGA
Source
FIFO
Dest
FIFO
After transfer, used source and destination buffers are cleared and new buffers are inserted.

## Slide 33: Example: Download
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
System + PCI
Host CPU
Main Memory
TEMAC
NIC
FPGA
Source
FIFO
Dest
FIFO
After transfer, used source and destination buffers are cleared and new buffers are inserted.

## Slide 34: Example: Download
FPGA CPU
PLB
Interrupt
Controller
DMA Engine
Local RAM
PCI Bridge
IntMain
IntFPGA
System + PCI
Host CPU
Main Memory
TEMAC
NIC
FPGA
Source
FIFO
Dest
FIFO
At all steps, interrupt coalescing is used to improve performance.

## Slide 35: Software Stack
FPGA CPU used to run OS and peripheral driver.
System based on two drivers, running on FPGA and host system.
FPGA driver:
  Controls the peripherals.
  Low-level driver based on available peripheral driver (only minor modifications needed).
  FPGA DMA Interface reused across different peripherals.
11/19
Notes: Usable on Point to Point bus

## Slide 36: Software Stack
FPGA CPU used to run OS and peripheral driver.
System based on two drivers, running on FPGA and host system.
Host driver:
  Forwards the data buffered on the FPGA to/from the Host OS.
  Host DMA Interface can be reused across different peripherals and is host OS independent.
  High-Level Driver is host OS dependent.
11/19

## Slide 37: Peripheral Virtualization
RT-Bridge supports peripheral virtualization.
Single peripheral (ex: Network Interface Card) can service different software partitions.
HW virtualization enforces strict timing isolation.
33

## Slide 38: Implemented Prototype
Host OS: Linux 2.6.29, FPGA OS: Petalinux (2.6.20 kernel).
Xilinx TEMAC 1Gb/s ethernet card (integrated on FPGA).
3 Smart Bridges, PCIe 250MB/s; contention at main memory level.
Optimized driver implementation with no software packet copy.
12/19
Notes: Say contention at memory level even with PCIe

## Slide 39: Flow Analysis
Main advantage: bus feasibility checked using well-known monoprocessor schedulability tests.
Servers are used to enforce transmission budgets for aperiodic traffic.
However, we pay in term of flow delay and on-bridge memory.
While a Real-Time Bridge is blocked, incoming network packets must be buffered in the FPGA RAM.
  How much buffer space is needed (backlog)?
  What is the maximum buffer time (delay)?
We devised a methodology based on real-time calculus to compute bounds on delay and buffer size.
13/19

## Slide 40: Evaluation
Experiments based on Intel 975X motherboard with 4 PCIe slots.
3 x Real-Time Bridges, 1 x Traffic Generator with synthetic traffic.
Rate Monotonic with Sporadic Servers.
Scheduling flows without reservation controller (block always low) leads to deadline misses!
Peripheral | Transfer Time | Budget | Period
RT Bridge | 7.5ms | 9ms | 72ms
Generator | 4.4ms | 5ms | 8ms
Utilization 1, harmonic periods.
Generator
RT-Bridge
RT-Bridge
RT-Bridge
17/19

## Slide 41: Evaluation
Experiments based on Intel 975X motherboard with 4 PCIe slots.
3 x Real-Time Bridges, 1 x Traffic Generator with synthetic traffic.
Rate Monotonic with Sporadic Servers.
Peripheral | Transfer Time | Budget | Period
RT Bridge | 7.5ms | 9ms | 72ms
Generator | 4.4ms | 5ms | 8ms
No deadline misses with reservation controller
Generator
RT-Bridge
RT-Bridge
RT-Bridge
17/19

## Slide 42: Reconfigurable Devices and Real-Time
Great deal of attention on reconfigurable FPGA for embedded and real-time systems
  Pro: HW logic is (often) more predictable than SW executing on complex microarchitectures
  Pro: HW logic is more efficient (per unit of chip area/power consumption) compared to GP CPU on parallel math crunching applications – somehow negated by GPU nowadays
  Cons: Programming the HW is more complex
Huge amount of research on synthesis of FPGA logic from high-level specification (ex: SystemC).
How to use it: static design
  Implement I/O, interconnects and all other PE on ASIC.
  Use some portion of the chip for a programmable FPGA processor.

## Slide 43: Reconfigurable FPGA
How to use it: dynamic design
  Implement I/O and interconnects as fixed logic on FPGA.
  Use the rest of the FPGA area for reconfigurable HW tasks.
HW Task
  Period, deadline, wcet as SW tasks.
  Additionally has an area requirement.
  Requirement depends on the area model.

## Slide 44: Area Model
2D model
  HW Tasks with variable width and height.
5/ 18
1D model
  HW Tasks have variable width, fixed height.
  Easier implementation, but possibly more fragmentation.

## Slide 45: Example: Sonic-on-a-Chip
Slotted area
  Fixed-area slots
Reconfigurable design targeted at image processing.
Dataflow application.
Some or all dataflow nodes are implemented as HW tasks.

## Slide 46: Main Constraints
Interconnects constraints
  HW tasks must be interfaced to the interconnects.
  Fixed wire connections: bus macros.
  The 2D model is very hard to implement.
Reconfiguration constraints
  With dynamic reconfiguration a HW task can be reconfigured at run-time, but…
  … reconfiguration takes a long time.
  Solution: no HW task preemption.
  However, we can still activate/deactivate HW tasks based on current application mode.

## Slide 47: The Management Problem
FPGA management problem
  Assume each task can be HW or SW
  Given a set of area/timing constraints, decide how to implement each task.
Additional trick: HW/SW migration
  Run-time state transfer between HW/SW implementation
t
CPU
HW
data load
reconfiguration
HW job
SW period
HW period
1. program ICAP
0. migrateSWtoHW
2. ICAP int
3. CMD_START
4. CMD_DOWNLOAD

## Slide 48: The Allocation Problem
If HW tasks have different areas (width or #slots), then the allocation problem is an instance of a bin-packing problem.
  Dynamic reconfiguration: additional fragmentation issues.
  Not too dissimilar from memory/disk block management..
Wealth of results for various area/execution models…
0
1
2
3
4
5
6
7
8
9
0/9
9/9
3/9
6/9
FPGA
CPU

## Slide 49: Assignments
Next Monday 8:00AM: literature review.
Fix/extend the introduction and project plan based on provided comments.
Include an extended comparison with related work.
  How each related work tackled your research problem.
  How you are going to tackle the problem.
  Why your approach is worthwhile compared to related work.
  What are the limits of your approach compared to related work.
  You do not need to describe your complete solution (or results), but do include some technical details – you need to show that you have a clear direction for the project.
  Of course you also need to show that you read the related work…

## Slide 50: Final
Final: scheduled for December 12
Let me know if you have any conflict.